# City of Portland

# Portland Bureau of Transportation

# Civil Engineering and Drafting Division (CED)

# CAD/Drafting Checklist

# for 30%, 60%, 95%, Final Plan Checks

(Use Navigation Pane in MSWord to see links to Sheet by Sheet Instructions.)

For Assistance, contact Chris Shearer, CED CADD Lead.

| PROJECT NO. | CAD TECH | DATE |
| --- | --- | --- |
| PROJECT NAME |  |
| DESIGN ENGINEER | COMPANY |

NOTES:

- Form Name: “Drafting Checklist 30-60-95-Final XXXXXXXX..doc”

- This form is intended to be used for all projects that are provided by CDCM CAD Section.

- Suggestions:

- -Could be updated/per project and used at bi-weekly drafting status meetings)

  - *Upload “dated copies” of this completed form to e-Builder upon milestone completions (…*work in progress)

- Typical Form Location (Destination):

      - II_Design\T00xxx – Project Name\CAD\PLAN_SHEETS\_DRAFTING AND PRINTING CHECKLIST\

      - And on PBOT Website, under Design Documents

- Copy Form From:

      - S:\_V_CDS Standards\3) Templates, Forms\_II_Design\CAD\PLAN_SHEETS\DRAFTING AND _PRINTING CHECKLIST)

- Complete this form by entering information above and checking boxes (double-click box) as items have been completed.

  - (STRIKE THRU if not applicable)

  - Coordinate any missing items with designers before checking boxes or striking thru.

Helpful to Use Navigation Pane

## General Requirements by Milestone

## 30-60-95 and Final (See respective color designation)

## 30% Review (1st Utility Notice)

Plan Set

Horizontal Alignments (Control Lines)

Profiles – centerline and/or left and right gutters (as applicable)

Typical section(s)

Utility notes

## 60% Review (2nd Utility Notice)  – Add to 30% items

Plan Set

Profiles – centerline and/or left and right gutters (as applicable)

Construction (bubble) notes

Horizontal Alignment Plans

Elevation Detail Plans (CED’s)

Ramps (with Monolithic Area Totals (SQ.FT. qty. & shading), driveways

Stormwater Plans (‘D’ sheets)

Retaining Wall Plans and Profiles

Permanent Striping Plans

Permanent Signing Plans (draft)  – minus Post Data Sheet

Illumination Plans

Traffic Signal Plans – Signalization, Detection and Interconnect Plans

## 95% Review and Final Reviews  – Add to 60% items

Plan Set

Details

Traffic Control Plan (construction staging)

Erosion Control Plan (gravel entrances, inlet protection, silt fences)

Permanent Signing – Post Data Sheet

Traffic Signal Plans – Removal Plan, Wiring Diagram, Details

Landscape Plans

(3rd Utility Notification issued through eBuilder/Roadrunner at Final PS&E)

## Specific Requirements by Milestone

## (applicable to noted milestone color as required)

## CITY TITLE BLOCK (CAD FILE)

(REQUIRED 30-60-95 and Final)

(Option 1: (pbot_std_tblk.dgn)

(*Option 2: odot-pbot-scff_cds_tblk.dgn)

Label/Edit:

Main Project Title (To Match eBuilder “Official Title”)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE)

Design Status Box placed.

## SHT 01 COVER

(REQUIRED 30-60-95 and Final)

(“PLOT_SHT_01A-01.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

“City of Portland Bureau of Transportation” (Line 1)

“Plans for Proposed Project (Line 2)

Type of improvements (Line 3) (and 3a if needed)

Program name (if applicable) (Line 3b)

Main Project Title (To Match eBuilder “Official Title”) (Line 4) (and 4a if needed)

“Multnomah County” (*w/Option 2-above) (Line 5)

Advertisement Month and Year (Line 6)

Sheet Project Title (To Match eBuilder “Official Title”)

Design Status Box

ADD:

Index of Sheets (optional - if it fits) or use SHT 01A-01 INDEX OF SHEETS.

Index of Standard Drawings (optional - if it fits) or use SHT 01A-01 INDEX OF SHEETS.

Overall length of project (< ¼ mile in feet; > ¼ mile in miles)

Location Map (Normally 1”=1000’, or 1”=2000’)  St. Names, EOP, RR, Water edge (gis)

North arrow

Bar scale (Normally 1”=1000’, or 1”=2000’)

Project limits (Beginning/End)

Street Names

Advisory note to excavators

Sheet Number

## SHT 01A-01 INDEX OF SHEETS

(REQUIRED 30-60-95 and Final)

(“PLOT_SHT_01A-01.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

ADD:

Index of Sheets (optional - if it fits) or use SHT 01A-01 INDEX OF SHEETS.

Index of Standard Drawings

## SHT. 1B  (SYMBOLS AND ABBREVIATIONS)

(REQUIRED 30-60-95 and Final)

(“PLOT_SHT_01B.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

All inclusive, pre-defined symbols and line types

ADD:

Custom Elements (as required in rare instances).

Sheet Number

## SHT. 1C  (SHEET LAYOUT PLAN)

(REQUIRED 30-60-95 and Final)

(“PLOT_SHT_01C.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Size to fit Layout Boxes. (may need multiple sheets., 1C-1, 1C-2, 1C-3 etc..)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

ADD:

Turn “on”  Layout Boxes (From “layout.dgn” Cad file)

Sheet call-out labels

Street Names

North Arrow

Bar Scale

Sheet Number

## SHT. 2A-1 TYPICAL SECTIONS

(REQUIRED 30-60-95 and Final)

(“PLOT_SHT_02A-01.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

ADD: SECTIONS (individual files) WHICH INCLUDE

Right-of-way lines

Easement lines

Centerlines: right-of-way/labeled.

Control lines w/labels.

Curb: type, exposure dimensions.

Pavement: width dimensions, cross slopes, information (subgrades base, wearing courses, sawcuts).

Sidewalks: widths, cross slopes, thicknesses, detail call-outs.

Lane widths, dimensioned.

Street trees, labeled.

Berm: widths, cross slopes, labeled.

Swale (if applicable): width, depth, side slopes, labeled.

Water mains, G.M.’s etc. (if applicable): locations, depths, labeled.

Back slopes, labeled.

Sub Title: Station range.

Sub Title: Street Name.

Typical Section Title: Labeled (Section bubble, numbered and cross referenced)

Scale labeled: (Scale: x/x” = 1’-0”)

Sheet Number

## SHT. 2B-1 TYPICAL SECTIONS

(REQUIRED 30-60-95 and Final)

## SHT. 2B-1 CONSTRUCTION DETAILS

(REQUIRED 60-95)

(“PLOT_SHT_02B-01.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

ADD: SECTIONS AND/OR DETAILS (individual files) WHICH INCLUDE

Right-of-way lines

Easement lines

Centerlines: right-of-way/labeled.

Control lines w/labels.

Curb: type, exposure dimensions.

Pavement: width dimensions, cross slopes, information (subgrades base, wearing courses, sawcuts).

Sidewalks: widths, cross slopes, thicknesses, detail call-outs.

Lane widths, dimensioned.

Street trees, labeled.

Berm: widths, cross slopes, labeled.

Swale (if applicable): width, depth, side slopes, labeled.

Water mains, G.M.’s etc. (if applicable): locations, depths, labeled.

Back slopes, labeled.

Sub Title: Station range.

Sub Title: Street Name.

Detail Title: Labeled (Detail bubble, lettered and cross referenced)

Scale labeled: (Scale: x/x” = 1’-0”)

Sheet Number

## SHT. 2C-1 TEMPORARY TRAFFIC CONTROL  (REQUIRED 95)

(REQUIRED  and Final)

(“PLOT_SHT_02C-01.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

ADD:

Raster Images

Sheet Number

Optional:

Detail Title: Labeled (Detail bubble, lettered and cross referenced)

Scale labeled: (Scale: x/x” = 1’-0”)

## SHT. 2D-1 EROSION CONTROL PLAN (REQUIRED 95)

(REQUIRED 95 and Final)

(“PLOT_SHT_02D-01.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

Turn “on” Information checklist (from “Existing” and “Improve”)

Right-of-way lines

Property lines

Easement lines

Street names

Addresses (from gis)

Vacant Lots

Lot or tax lot numbers

Existing features (Survey & GIS) utilities, power poles, guy wires and anchors, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, walls etc..

Improve features: utilities, power poles, guy wires and anchors, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, walls etc..

Sawcuts

Horizontal scale (1”=10’, 20’, 30’)

Control Lines w/stationing, ticks and labels

Clearing Limits (if extend beyond limits stated in Standard Specifications)

Cut and fill lines (if applicable)

Patterning for concrete, AC, swales/planter boxes, planting strip

Improve Inlets/Leads:  Grayed out…(reference D-xx sheets).

Street trees: Station location/offset

Signal poles

ADD:

Match lines (with stations and sheet reference)

North arrow

Bar scale

Construction Bubble Notes Legend

Construction Bubble Notes

Inlet protection

Sediment fence

Gravel construction entrances

Sheet Number

## SHT. 2E-1, 2E-2, 2E-3 HORIZONTAL ALIGNMENT PLAN

(REQUIRED 60-95 and Final)

(“PLOT_SHT_02E-01.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

Turn “on” Information checklist (from “Existing” and “Improve”)

Right-of-way lines

Property lines

Easement lines

Street names

Addresses (from gis)

Vacant Lots

Inlets

Lot or tax lot numbers

Existing features: Back of curbs

Stationing w/ticks

Match lines (with stations and sheet reference)

ADD:

Match lines (with stations and sheet reference)

North arrow

Bar scale

Survey Control Reference call outs: curve data; PI, PC, PT, PRC, PCC

Control Lines w/stationing and labels (northings/eastings at ends of lines)

Curve data D,R,T,L (control lines)

Centerline equations for all intersecting streets

Cul de sacs: Radius, profile stationing, high point

Bearings and distances (along control lines)

Dimensions between control lines at PI, PC, PT, PRC, PCC points

Sheet Number

## SHT. 2F-1 ELEVATION DETAIL PLAN

(REQUIRED 60-95 and Final)

(“PLOT_SHT_02F-01.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

Turn “on” Information checklist (from “Existing” and “Improve”)

Right-of-way lines

Property lines

Easement lines

Street names

Control Lines w/stationing and labels

Signal poles

Back of curbs

Stationing w/ticks

Scale:  1”=5’

Improve Inlets/Leads:  Grayed out…(reference D-xx sheets).

Street name or intersection references

Truncated domes on ramps

Ramps (with Monolithic Area Legend Totals (SQ.FT. qty. & shading)

ADD:

North arrow

Bar scale

Match lines (with stations and sheet reference)

Survey Control Reference call outs: curve data; PI, PC, PT, PRC, PCC

Northings/Eastings (at ends of control lines)

Detail Title: Labeled (Detail bubble, lettered and cross referenced)

Scale labeled: (Scale: x/x” = 1’-0”)

Survey Control References: PC, PT, PRC, PCC

Dimensions for driveways, driveways connections, wings, ramps, landings

Design elevations for driveways, driveway connections, wings, ramps, landings, grade breaks – along curb line, include elevations for gutter (noted with a “g”) and top of curb

Inlets

Drainage (flow arrows in gutters)

## SHT. 2G-1 CONCRETE SCORING PLAN

(REQUIRED 60-95 and Final)

(“PLOT_SHT_02G-01.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

Turn “on” Information checklist (from “Existing” and “Improve”)

Right-of-way lines

Property lines

Easement lines

Street names

Addresses (from gis)

Vacant Lots

Lot or tax lot numbers

Existing features (Survey & GIS) utilities, power poles, guy wires and anchors, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, etc..

Improve features: utilities, power poles, guy wires and anchors, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, etc..

Sawcuts

Horizontal scale (1”=10’, 20’, 30’)

Control Lines w/stationing, ticks and labels

Clearing Limits (if extend beyond limits stated in Standard Specifications)

Cut and fill lines (if applicable)

Patterning for concrete, AC, swales/planter boxes, planting strip

Improve Inlets/Leads:  Grayed out…(reference D-xx sheets).

Signal poles

ADD:

Match lines (with stations and sheet reference)

North arrow

Bar scale

Construction Bubble Notes Legend

Construction Bubble Notes

Inlet protection

Sediment fence

Gravel construction entrances

Sheet Number

## SHT. 3,4,5 STREET PLANS

(REQUIRED 30-60-95 and Final)

(“PLOT_SHT_03.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

Turn “on” Information checklist (from “Existing” and “Improve”)

Right-of-way lines

Property lines

Easement lines

Street names

Addresses (from gis)

Vacant Lots

Lot or tax lot numbers

Existing features (Survey & GIS) utilities, power poles, guy wires and anchors, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, walls, etc..

Improve features: utilities, power poles, guy wires and anchors, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, walls, etc..

Sawcuts

Horizontal scale (1”=10’, 20’, 30’)

Control Lines w/stationing, ticks and labels

Clearing Limits (if extend beyond limits stated in Standard Specifications)

Cut and fill lines (if applicable)

Patterning for concrete, AC, swales/planter boxes, planting strip

Existing trees in right-of-way – Save or Remove note

Save Tree – root inspection note (if needed)

Driveways: Station, width size label w/bubble notes.

Improve Inlets/Leads:  Grayed out…(reference D-xx sheets).

Street trees: Station location/offset

Signal poles

Tree protection fence

ADD:

Match lines (with stations and sheet reference)

North arrow

Bar scale

Construction Bubble Notes Legend

Construction Bubble Notes

Sheet Number

## SHEET 3A,4A,5A  STREET PROFILE

(REQUIRED 30-60-95 and Final)

(“PLOT_SHT_03A.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

ADD: PROFILES (individual files/referenced) WHICH INCLUDE

Existing grade

Proposed grade

Match lines (with stations and sheet reference)

Profile grid border

Profile grid major

Profile grid minor

Water mains, G.M.’s etc. (if applicable): locations, depths, labeled.

Sub Title: Alignment Name

Profile Title: Labeled (Detail bubble, lettered and cross referenced)

Scale labeled: Scale: 1" =  1' Vert. 1" = 10' Horiz.

ADD:

Sheet Number

## SHT. D-1  (STORMWATER FACILITIES OVERVIEW)

(REQUIRED 60-95 and Final)

(“PLOT_SHT_D-01.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Size to fit Layout Boxes. (may need multiple sheets., 1C-1, 1C-2, 1C-3 etc..)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

ADD:

Turn “on”  Boundary Stormwater Facility (From “bes_shading.dgn” Cad file)

Sheet call-out labels (if required)

Street Names

North Arrow

Bar Scale

Sheet Number

## SHT. D-2 DRAINAGE NOTES AND TABLES

(REQUIRED 60-95 and Final)

(“PLOT_SHT_D-02.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

ADD: DETAILS (individual files) WHICH INCLUDE

Raster Images

Optional:

Sheet Number

## SHT. D-3, D-4, D-5 STORMWATER PLANS

(REQUIRED 30-60-95 and Final)

(“PLOT_SHT_D-03.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

Turn “on” Information checklist (from “Existing” and “Improve”)

Right-of-way lines

Property lines

Easement lines

Street names

Addresses (from gis)

Vacant Lots

Lot or tax lot numbers

Existing features (Survey & GIS) utilities, power poles, guy wires and anchors, overhead power lines, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, etc..

Improve features: utilities, power poles, guy wires and anchors, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, walls, etc..

Sawcuts

Horizontal scale (1”=10’, 20’, 30’)

Control Lines w/stationing, ticks and labels

Clearing Limits (if extend beyond limits stated in Standard Specifications)

Cut and fill lines (if applicable)

Patterning for concrete, AC, swales/planter boxes, planting strip

Existing trees in right-of-way – Save or Remove note

Save Tree – root inspection note (if needed)

Driveways: Station, width size label w/bubble notes.

Improve Inlets/Leads:  Grayed out…(reference D-xx sheets).

Street trees: Station location/offset

Signal poles

Tree protection fence

ADD:

Match lines (with stations and sheet reference , if needed)

Inlets: station, offset, type, rim elevation

Inlet leads: pipe type, diameter, length (plan view), profile

North arrow

Bar scale

Construction Bubble Notes Legend

Construction Bubble Notes

Sheet Number

## SHT. BR-XX BRIDGE PLANS

(REQUIRED 30-60-95 and Final)

(“PLOT_SHT_BR-XX.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

ADD: DETAILS (individual files) WHICH INCLUDE

Right-of-way lines.

Centerlines: right-of-way/labeled.

Control lines w/labels.

Curb: type, exposure dimensions.

Pavement: width dimensions, cross slopes, information (subgrades base, wearing courses, sawcuts).

Sidewalks: widths, cross slopes, thicknesses, detail call-outs.

Lane widths, dimensioned.

Street trees, labeled.

Berm: widths, cross slopes, labeled.

Swale (if applicable): width, depth, side slopes, labeled.

Water mains, G.M.’s etc. (if applicable): locations, depths, labeled.

Back slopes, labeled.

Sub Title: Station range.

Sub Title: Street Name.

Detail Title: Labeled (Detail bubble, lettered and cross referenced)

Scale labeled: (Scale: x/x” = 1’-0”)

Sheet Number

Match lines (with stations and sheet reference , if needed)

## SHT. R-1, R-2, R-3 RETAINING WALL W1-L PLAN AND PROFILE

(REQUIRED 60-95 and Final)

(“PLOT_SHT_R-01.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

Turn “on” Information checklist (from “Existing” and “Improve”)

Right-of-way lines

Property lines

Easement lines

Street names

Addresses (from gis)

Vacant Lots

Lot or tax lot numbers

Existing features (Survey & GIS) utilities, power poles, guy wires and anchors, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, walls etc..

Improve features: utilities, power poles, guy wires and anchors, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, walls etc..

Sawcuts

Horizontal scale (1”=10’, 20’, 30’)

Control Lines w/stationing, ticks and labels

Clearing Limits (if extend beyond limits stated in Standard Specifications)

Cut and fill lines (if applicable)

Patterning for concrete, AC, swales/planter boxes, planting strip

Improve Inlets/Leads:  Grayed out…(reference D-xx sheets).

Street trees:

Signal poles

ADD:

Match lines (with stations and sheet reference)

North arrow

Bar scale

Construction Bubble Notes Legend

Construction Bubble Notes

Inlet protection

Sediment fence

Gravel construction entrances

Sheet Number

## SHT. R-xx RETAINING WALL DETAILS

(REQUIRED 60-95 and Final)

(“PLOT_SHT_R-xx.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

ADD: DETAILS (individual files) WHICH INCLUDE

Right-of-way lines.

Centerlines: right-of-way/labeled.

Control lines w/labels.

Curb: type, exposure dimensions.

Pavement: width dimensions, cross slopes, information (subgrades base, wearing courses, sawcuts).

Sidewalks: widths, cross slopes, thicknesses, detail call-outs.

Lane widths, dimensioned.

Street trees, labeled.

Berm: widths, cross slopes, labeled.

Swale (if applicable): width, depth, side slopes, labeled.

Water mains, G.M.’s etc. (if applicable): locations, depths, labeled.

Back slopes, labeled.

Sub Title: Station range.

Sub Title: Street Name.

Detail Title: Labeled (Detail bubble, lettered and cross referenced)

Scale labeled: (Scale: x/x” = 1’-0”)

Sheet Number

## SHT. RW-01 RIGHT OF WAY PLAN

(AS-REQUIRED 60-95 and Final)

(“PLOT_SHT_RW-01.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

Turn “on” Information checklist (from “Existing” and “Improve”)

Right-of-way lines

Property lines

Easement lines

Street names

Addresses (from gis)

Vacant Lots

Lot or tax lot numbers

Existing features (Survey & GIS) utilities, power poles, guy wires and anchors, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, walls, etc..

Improve features: utilities, power poles, guy wires and anchors, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, walls, etc..

Sawcuts

Horizontal scale (1”=10’, 20’, 30’)

Control Lines w/stationing, ticks and labels

Clearing Limits (if extend beyond limits stated in Standard Specifications)

Cut and fill lines (if applicable)

Patterning for concrete, AC, swales/planter boxes, planting strip

Improve Inlets/Leads:  Grayed out…(reference D-xx sheets).

Street trees:

Signal poles

Tree protection fence

ADD:

Match lines (with stations and sheet reference)

North arrow

Bar scale

Construction Bubble Notes Legend

Construction Bubble Notes

Sheet Number

## SHT S-01, S-02, S-03 PERMANENT SIGNING AND STRIPING PLAN

(REQUIRED 60-95 and Final)

(“PLOT_SHT_S-01.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

Turn “on” Information checklist (from “Existing” and “Improve”)

Right-of-way lines

Property lines

Easement lines

Street names

Addresses (from gis)

Vacant Lots

Lot or tax lot numbers

Existing features (Survey & GIS) utilities, power poles, guy wires and anchors, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, walls, etc..

Improve features: utilities, power poles, guy wires and anchors, trees, landscape, structures, curbs, sidewalks, driveways, pavement, gravel, inlets, fences, mailboxes, signs, signals, streetlights, pavement markings, railroad tracks, hydrants, meter boxes, walls, etc..

Horizontal scale (1”=10’, 20’, 30’)

Control Lines w/stationing, ticks and labels

Patterning for concrete, AC, swales/planter boxes, planting strip

Existing trees in right-of-way – Save or Remove note

Improve Inlets/Leads:

Street trees: Station

Signal poles

ADD:

Match lines (with stations and sheet reference)

North arrow

Bar scale

Construction Bubble Notes Legend

Construction Bubble Notes

Sheet Number

## SHT S-XX PERMANENT SIGNING LEGEND

(REQUIRED 60-95 and Final)

(“PLOT_SHT_S-XX.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

ADD:

Raster Images

Sheet Number

Optional:

Detail Title: Labeled (Detail bubble, lettered and cross referenced)

Scale labeled: (Scale: x/x” = 1’-0”)

## SHT. S-LAST SIGN AND POST DATA TABLE

(REQUIRED 60-95 and Final)

(“PLOT_SHT_S-XX.dgn”)

City title block (with all items labeled/checked). From pbot_std_tblk.dgn (above)

Turn “on” (from pbot_std_tblk.dgn) (above)

Sheet Project Title (To Match eBuilder “Official Title”)

Project Number (Include BES # If Known)

1/4 Section(s)

Designed By: (First Name Initial and Last Name)

Cad By: (First Name Initial and Last Name)

Checked By: (First Name Initial and Last Name)

Date Approved: (Mo. Year)

Division Engineer: (First Name Initial and Last Name)

PE Stamp and Expiration Date

SUPERVISING ENGINEER and REG. PROF. ENGR. NO. xxxxxPE

PE #’s (Supervising Engineer & City Engineer = 51538PE

Design Status Box

ADD:

Raster Images

Sheet Number

Optional:

Detail Title: Labeled (Detail bubble, lettered and cross referenced)

Scale labeled: (Scale: x/x” = 1’-0”)

## ILLUMINATION PLANS (SHEET IL-XX)   (NON-CDS)

(AS-REQUIRED 60-95 and Final)

Details

Plans

## TRAFFIC SIGNAL PLANS (SHEET TS-XX)   (NON-CDS)

(AS-REQUIRED 60-95 and Final)

Details

Plans

## LANDSCAPING PLANS (SHEET L-XX)   (NON-CDS)

(AS-REQUIRED 60-95 and Final)

Details

Plans

## IRRIGATION PLANS (SHEET IR-XX)  (NON-CDS)

(AS-REQUIRED 60-95 and Final)

Details

Plans

## WATER PLANS (SHEET W-XX)  (NON-CDS)

(AS-REQUIRED 60-95 and Final)

Details

Plans